## Slide 1: Designing RF antennas with Ansys HFSS
Huan Q. Bui
ZGS July 7, 2023

## Slide 2: Why RF antennas?
RF evaporation

## Slide 3: Why RF antennas?
RF evaporation
Spin manipulation

## Slide 4: Why RF antennas?
RF evaporation
Spin manipulation
Make/break molecules
Cheng-Hsun, W., et al., Phys. Rev. Lett 109 (2012): 085301.

## Slide 5: Why RF antennas?
RF evaporation
Spin manipulation
Tune molecular interactions (promised ZGS?)
Make/break molecules
Schindewolf, Andreas, et al. Nature 607.7920 (2022): 677-681.
Cheng-Hsun, W., et al., Phys. Rev. Lett 109 (2012): 085301.

## Slide 6: RF antennas in nature

## Slide 7: RF antennas in the lab (Fermi1)
F1 outer antenna
for Na RF Evap
PC: Alex
CHW thesis
for K spin
manipulation

## Slide 8: RF antennas in the lab (Fermi1)
F1 outer antenna
for Na RF Evap
PC: Alex
CHW thesis
for K spin
manipulation
What do your antennas look like?

## Slide 9: Antenna design considerations
Type & material
Operating frequency range
Polarization of radiation
Antenna matching (“resonance”)
Tunability
Environmental effects
Cost (time and money)

## Slide 10: Antenna design considerations
Type & material
Operating frequency range
Polarization of radiation
Antenna matching (“resonance”)
Tunability
Environmental effects
Cost (time and money)
Want:
  Simulations before prototyping
  Understanding of antenna behavior
  Confidence in design
  Good selection of parts
  Reproducibility
Don’t want:
  Design by trial and error
  Not foreseeing unexpected behaviors
  Voo-doo! Not reproducible

## Slide 11: Ansys HFSS
Free*, powerful 3D EM solver
Relatively easy to learn and use:
  Watch tutorials (YT/Ansys classes)
  Build antenna
  Set up solution and solve
  Optimize
Alternatives:
  COMSOL (very not free, IS&T has no license)
  MATLAB (not enough features)

## Slide 12: Modeling a waveguide antenna with Ansys HFSS in 10 steps

## Slide 13: Step 1: Waveguide antenna requirements & dimensions
Operational frequency: 5.640 GHz
Tunable polarization
Radiation with high directivity
Rectangular waveguide antenna

## Slide 14: Step 1: Waveguide antenna requirements & dimensions
Operational frequency: 5.640 GHz
Tunable polarization
Radiation with high directivity
Rectangular waveguide antenna
Width: needs cutoff frequency of TE01 mode < 5.64 GHz  a = 33 mm
Length: To be optimized, but set to 58 mm
Feeds: Naively, 2 perpendicular feeds. 13 mm from backwall, 9.5 mm tall
Hole in the backwall for the MOT beam
Inspired by Xing-Yan Chen et al, Nature, volume 614, pages 59–63 (2023)

## Slide 15: Step 2: Build the antenna in Ansys HFSS
Parametrize!
Feed dimensions: SMA stub connectors
Can specify materials

## Slide 16: Step 2: Build the antenna in Ansys HFSS

## Slide 17: Step 3: Define boundary conditions

## Slide 18: Step 3: Define boundary conditions
Radiation box
  Defines FEM volume
  Allows energy to radiate out of solution space
  Material: vacuum, air, etc.

## Slide 19: Step 4: Define excitations

## Slide 20: Step 4: Define excitations
… to get antenna’s response: S-parameters, fields, etc. = plugging in the VNA
Excitation on coaxial structure
With multiple ports, can specify:
  Relative phases
  Relative power (W, dBm, etc.)
  Port normalization (Zout of source)

## Slide 21: Step 4: Define excitations
Port renormalization:
  Enabled: port Z is fixed
  Disabled: port Z calculated from design
  Good practice: design connectors to specified impedance, but normalize anyway

## Slide 22: Step 5: Set up analysis

## Slide 23: Step 5: Set up analysis
What to calculate?
  Antenna response at different frequencies (S-parameters)
  E-field strength & polarization in a region/at a point
  Radiation pattern
  Directivity
  …
Vacuum box

## Slide 24: Step 5: Set up analysis
What to set up?
  Solution frequency
  Frequency sweep (range, # of points)
  Advanced options:
    Calculate derivatives wrt design parameters
    Solver (tolerance, # of adaptive solution passes, etc.)
    Optimization
    …

## Slide 25: Step 6: Validate and solve

## Slide 26: Step 7: View results
S-parameters
S11
S21

## Slide 27: Step 7: View results
3D radiation pattern & directivity

## Slide 28: Step 7: View results
E-field strength and polarization

## Slide 29: Step 7: View results
E-field strength and polarization

## Slide 30: Step 7: View results
E-field strength and polarization

## Slide 31: Step 8: Study
Polarization tuning
Counter-intuitive power ratio

## Slide 32: Step 8: Study
Only one probe feed
 expect linear polarization
x
y
Something wrong with the model?
Where does Ey come from?
…

## Slide 33: Step 8: Study
Something wrong with the model?
Test 1: make diagonal polarizations
as expected

## Slide 34: Step 8: Study
Something wrong with the model??
Test 2: Effect of inactive probe feed on active probe feed
x
y
Likely the antenna’s geometry

## Slide 35: Step 8: Study
Something wrong with the model??
Test 3: Restore the antenna symmetry by adding probe feeds
It is the antenna’s geometry
Inactive
Active
Dual-polarized commercial antenna

## Slide 36: Aside: A real antenna
pc: Munich group & Martin
Power ratio for CP = 1 : 2

## Slide 37: Aside: A different antenna
SW’s cloverleaf antenna
46 MHz Rabi frequency with NaCs, or E = 33 kV/cm

## Slide 38: Step 9: Optimize/Revise
Can we get the best of both worlds??
+

## Slide 39: Step 9: Optimize/Revise
Four-feed design:
Intuitive and easy polarization tuning
High directivity
High reproducibility
More E for less $$$
Standard SMA stub connectors

## Slide 40: Step 9: Optimize/Revise
S-parameters

## Slide 41: Step 9: Optimize/Revise
Radiation pattern & directivity

## Slide 42: Step 9: Optimize/Revise
E-field strength and polarization

## Slide 43: Step 9: Optimize/Revise
E-field strength and polarization
Intuitive polarization tuning!
E ~ 30 V/cm

## Slide 44: Step 9: Optimize/Revise
Environmental effects? Say… a chunk of metal is nearby?
Many properties are modified: resonance, directivity, max E, etc.
E = 22 V/cm

## Slide 45: Step 9: Optimize/Revise
Other things to consider:
  Material
  Cost/ease of production
  Ease of installation
v0

## Slide 46: Step 10: Finalize
... make one and test it
5.64 GHz
< -14 dB
Tested using Libre VNA

## Slide 47: Summary:
Antenna requirements & dimensions
Build it in Ansys HFSS
Define boundary conditions
Define excitations
Set up analysis
Validate and solve
View results
Study
Optimize
Finalize

## Slide 48: Summary:
Antenna requirements & dimensions
Build it in Ansys HFSS
Define boundary conditions
Define excitations
Set up analysis
Validate and solve
View results
Study
Optimize
Finalize
Do things work as expected?
Effect on the choice of RF components?
What to do to improve antenna? (how to tune in lab)
…

## Slide 49
The end